## Slide 1
Preoperative localization of non-palpable breast and axillary lesions using RFID LOCALIZER
Kanavidis Prodromos1, Sakarellos Panagiotis1, Vagios Ilias1, Panagi Christiana1, Lanitis Sophocles2, Kontos Michalis1
1 1st Surgical Dept., Laikon Hospital, National and Kapodistrian University Of Athens, Greece
2 2nd Surgical Dept. and Unit of Surgical Oncology “Korgialenio – Benakio”, Red Cross Hospital, Greece
Introduction
Guidewires and metal markers have been in use for the localization of breast lesions and axillary lymph nodes for decades.
Recent technological advancements have introduced radioactive and magnetic seeds, as well as radar and RFID based devices, with equivalent results and obvious advantages.
This prospective cohort investigates the efficacy of RFID LOCALIZER for the localization of:
non-palpable breast lesions, and
infiltrated axillary lymph nodes, scheduled for neoadjuvant treatment
Parameters include placement efficiency, ease of use, safety and operative outcomes.
Materials and methods
Women with non-palpable breast lesions (short-term) or breast cancers planned for neoadjuvant chemotherapy (long-term), or women planned for targeted axillary dissection (TAD) were included.
Data collected included demographic parameters, tumor location, histopathology, duration of the insertion procedure, distance from lesion, ease of use and complications.
Operational parameters recorded were length of time from placement to surgery, duration of surgery, identification and retrieval rates, marker migration, difficulty locating the marker, final histopathology, resection margins and patient morbidity.
31 patients
21 patients with 1 breast marker +
3 patients with 2 markers
7 patients with 1 lymph node marker
Results
34 markers were inserted in 31 patients between June 2021 and April 2023 (Table 1). Mean placement time was 10.8 minutes for breast lesions and 6.4 minutes for axillary lymph nodes, with 0 complications. Bracketing was employed in 3 patients (12.5%), using two markers.
In 19 of 24 breast lesions the marker was placed within the lesion (79.1%), and the overall mean distance of the device from the lesion margin was 1.2mm. In 5 of 7 lymph nodes the marker was placed inside the lymph node (71.4%) and the overall mean distance of the device from the edge of the lymph node was 0.57mm.
Surgical operation has been completed for 21 of the patients so far (67.7%),
No marker migration noted (0%).
Mean duration of surgery: 100 minutes
Mean distance of marker from tumor margin on pathology 1.2mm (range 0-7mm).
All tumors had clear resection margins (R0)
Operative morbidity:
5 seromas (23.8%),
1 hematoma (4.8%)
1 fat necrosis (4.8%).
No patient mortality was observed (0%)
Marker placement | 
Breast | 24 (77.4%)
Axilla | 7 (22.6%)
Guidance | 
Ultrasound | 29 (93.5%)
Mammography | 2 (6.5%)
Breast (24) | 
Non-Palpable | 14 (58.3%)
Palpable | 10 (41.7%)
Long-term | 10 (41.7%)
Lymph nodes (7) | 
Long-term | 6 (85.7%)
Table 1. Patient Characteristics
Conclusion
fast clip application,
minimal complications,
quick and easy intraoperative detection,
no loss of markers
excellent identification and retrieval rates
precise tumor excision with negative resection margins.
Therefore, it is a versatile technique applicable to both breast lesions and axillary lymph nodes, with no time constraints, improving operating theater logistics and patient / doctor satisfaction.
National and Kapodistrian University Of Athens